Treatment and Use of Insecticide-Treated Mosquito Nets

# Why use Insecticide-Treated Mosquito Nets?

- Malaria and certain other diseases are transmitted by the bite of mosquitoes. Pregnant women, babies and young children are at the greatest risk of dying of malaria.

- Ordinary untreated mosquito nets provide limited physical barrier between mosquito and man and protection as they may still bite through the net or get inside the net following improper use.

- Mosquito nets treated with insecticides provide better and effective protection by keeping away mosquitoes as well as killing them. An insecticide-treated mosquito net also kills or keeps away other nuisance insects – cockroaches, bedbugs, houseflies, fleas, etc.

# How to treat the net – 10 Easy Steps for Mass Treatment

- Mass treatment is done at fixed/designated sites.

- Insecticide treatment is recommended for synthetic nets (nylon, polyester), as treatment of cotton nets is not cost-effective and effect of insecticide is not long lasting.

Step 1: Collect the necessary equipment

The necessary equipment consists of: mosquito nets, insecticide, basin, measuring container, rubber gloves, soap.

- Make sure the net is washed/cleaned before treatment.

- Preferably, nets should be treated outdoors in the shade. If treatment is to be carried out indoors, a room with open windows should be used.

- Use basin, gloves that are not used for any other purpose.

Step 2: Put on protective gloves before treating nets

Step 3: Measure the correct amount of water

The amount of water needed depends on the net material. Regardless of the size and shape of net, the amount of water required for:

- One synthetic net (nylon, polyester) – ½ litre (if the net is very large, more water may be needed).

    - If measuring container comes with insecticide, use it to measure water. Otherwise, use any measuring container, that is not used for food, drinks, medicines.

Step 4: Measure the correct amount of insecticide

- The amount of insecticide or “dose” needed to treat a net depends on type of insecticide used.  Follow instructions on the container, sachet, packet. Generally, 10-15 ml of insecticide is required to treat one net.

  - [BIS Number of Liquid Synthetic Pyrethroid used for treatment of Bed Nets -

i) Deltamethrin – IS14411: 1996; ii) Cyfluthrin – IS14156: 1994].

- Store leftover insecticide in its original container, in the dark and away from children.

Step 5: Mix the water and insecticide thoroughly by gloved hands in basin

Step 6: Treatment of nets

- Always treat one net at a time.

- Put the net in the basin containing water and insecticide.

- Soak the net long enough to ensure that all parts of the nets are impregnated.

- Take out the nets and allow excess liquid to drip back.

- Do not wring the treated net.

Step 7: Drying the nets

## Let the net dry flat in the shade on plastic sheets.

- Later, the net can be hung up to finish drying in the shade.

Step 8: Disposal of leftover mixture of water and insecticide and insecticide containers

- Following treatment of all available nets, leftover mixture of water and insecticide, if any, may be used to treat curtains.

- Otherwise, dispose the liquid in the toilet or a hole away from habitation, animal shelters, drinking water sources, ponds, rivers, streams.

- Destroy empty insecticide containers, sachets, packets and/or bury in a hole away from habitation, animal shelters, drinking water sources, ponds, rivers, streams.

Step 9: Washing and cleaning of hands, equipments

- Wash equipments (basin, measuring container) with lots of water while wearing protective gloves.

- Wash gloves (if non-disposable ones are used)] with soap and lots of water, or dispose with insecticide containers.

- Wash hands with soap and lots of water.

Step 10: Washing and re-treatment of nets

- Washing removes insecticide from the net. So, wash the nets as seldom as possible and gently with soap and cold water and dry flat on plastic sheet in shade.

- Do not wash/rinse treated net in or near drinking water sources, ponds, lakes, rivers, streams. Dispose of water for washing/rinsing in the toilet or in a hole away from habitation, animal shelters, drinking water sources, ponds, rivers, streams

  - Nets must be re-treated again after it has been washed three times. Or, at least once a year even if it is not washed, preferably just before the rainy season. Nets may be treated twice a year in areas that have a lot of mosquitoes all year long.

Remember: Use the insecticide-treated net every night, all year round, even if mosquitoes are not seen/heard. Preferably, everyone should sleep under a treated mosquito net. Or, at least pregnant women and children under five years must sleep under treated net. Insecticides used for mosquito nets are not harmful to people, if used correctly. Direct skin contact with the insecticide on a still wet net may cause a tingling sensation on the skin. This is not harmful, even for small children. After treatment, the net may smell of insecticide. This will go away in a few days and is not harmful to people who sleep under the net.